## Slide 1
CSC2231 COMPUTER ARCHITECTURE
Lecture slides 2
Computer Architecture and Organization
Ismail Abu Zibiri

## Slide 2: Performance Issues
Over the Years, The cost of computing systems continues to drop dramatically, while the performance and capacity of those systems continue to rise equally dramatically. Today’s laptops have the computing power of an IBM mainframe from 10 or 15 years ago. Thus, we have virtually “free” computer power. Processors are so inexpensive that we now have microprocessors we throw away.
Microprocessor Speed: What gives Intel x86 processors or IBM mainframe computers such mind-boggling power is the relentless pursuit of speed by processor chip manufacturers. The evolution of these machines continues to bear out.
The quest for better performance gives rise to the following techniques use by the processor.

## Slide 3: Processor

## Slide 4: Performance
The execution of an instruction involves multiple stages these includes.
Fetch the instruction
Detect the instruction
Execute the instruction
Pipelining: This enables a processor to work simultaneously on multiple instruction at same time by performing a different stage of each instruction at same time.
The processor overlaps operation by moving data's of instruction into a conceptual pipe with all stages been executed simultaneously.
When an instruction is on decode another is on execute.

## Slide 5: Performance
Branch Prediction: This process looks ahead in the instruction code fetch from memory and predicts which instruction or group of instructions are likely to be executed next. If the processors guess right most of the time, it can pre-fetch the correct instruction and buffer them so that the processor is kept busy.
Super Scale Execution: This is the ability to issue more than one instruction in every processor clock cycle. In effect multiple parallel pipeline are used.
Data Flow Analysis: The processor analyses which instruction are dependent on each others result or data to create an optimal schedule of instruction
Speculative Execution: combining both branch prediction and data flow analysis, some processor execute instruction ahead or their actually appearance in the program execution.
These and many more helps the processor very fast and keeps the process busy.

## Slide 6: Performance Balance
While processor power has raced ahead at breakneck speed, other critical components of the computer have not kept up. The result is a need to look for performance balance: an adjustment/tuning of the organization and architecture to compensate for the mismatch among the capabilities of the various components.
If memory or the pathway fails to keep pace with the processor’s insistent demands, the processor stalls in a wait state, and valuable processing time is lost.
A system architect can attack this problem in a number of ways, all of which are reflected in contemporary computer designs.

## Slide 7: Performance Balance
Increase the interconnect bandwidth between processors and memory by using higher-speed buses and a hierarchy of buses to buffer and structure data flow.
Reduce the frequency of memory access by incorporating increasingly complex and efficient cache structures between the processor and main memory. This includes the incorporation of one or more caches on the processor chip as well as on an off-chip cache close to the processor chip.
Change the DRAM interface to make it more efficient by including a cache1 or other buffering scheme on the DRAM chip.

## Slide 8: Execution Cycle
In evaluating processor hardware and setting requirements for new systems, performance is one of the key parameters to consider, along with cost, size, security, reliability, and, in some cases, power consumption.
In measuring processor and performance speed we look at some traditional measures of processor speed.
Clock Speed/Clock Circle: Operations performed by a processor, such as fetching an instruction, decoding the instruction, performing an arithmetic operation, and so on, are governed by a system clock. Typically, all operations begin with the pulse of the clock. Thus, at the most fundamental level, the speed of a processor is dictated by the pulse frequency produced by the clock, measured in cycles per second, or Hertz (Hz).
Everything computer does must be completed before the start of the next cycle (altho program execution could be pipelined – split up) – A machine running at 5GHz receives 5 x 109 clock signals per second (one pulse lasts 0.0000000005 seconds)

## Slide 9: Execution Cycle
The execution of an instruction involves a number of discrete steps, such as fetching the instruction from memory, decoding the various portions of the instruction, loading and storing data, and performing arithmetic and logical operations. Thus, most instructions on most processors require multiple clock cycles to complete. Some instructions may take only a few cycles, while others require dozens. In addition, when pipelining is used, multiple instructions are being executed simultaneously.
Time
Usually called the Fetch-Decode-Execute cycle

## Slide 10: Instruction Cycle
Instruction Cycle
We are all familiar with the clock cycle
Instruction execution cycle is triggered by the clock cycle
  Every stage of the instruction cycle is triggered by successive clock pulses
  Exact timing depends on the details of a machine type
  Complete instruction cycle usually takes several clock cycles to execute
Instruction cycle is divided into several stages
  In some machines, some stages are executed simultaneously
  The stages are common to most architectures

## Slide 11: Instruction Cycle
The steps that are followed when an instruction is executed are:
  Inspect the program counter (PC) to find the address of the next instruction
  Load the next instruction from the memory into the instruction register (IR)
  Update the PC to point the next instruction to be fetched
  Determine the type of instruction fetched
  If the instruction requires data from the memory, determine its address
  Fetch the data from memory into one of the CPU registers
  Execute the instruction
  Return to step a. for the next instruction

## Slide 12: Starting a Program
When a piece of code is run, the first thing that must be done is loading the code into memory
Once in memory, it can be executed
Instructions and data associated with program will each occupy a block of memory.
Exact location is determined by operating system
Memory address of the 1st instruction is called the entry- point
Running a new piece of code commences by loading the
entry-point into PC
PC = entry_point;

## Slide 13: Executing an Instruction
The entry-point is only the address of the first instruction (we, however need the instruction itself)
At the start of the next clock cycle, the CPU issues a request to the memory (thru the load/store unit)
  Load/store unit sends the memory address and a request to read from
the memory thru the address bus
Later, the instruction will be received from the memory by the load/store unit
  The instruction is put into the Instruction Register (IR)
IR = memory(PC);
  How long this takes depends on how fast the memory is
    Could be just in time for next clock cycle
    Could be many cycles later (if the instruction is in slow memory)
At this point, the value of the PC is changed to point to the next instruction
  Usually, this is just an increment

## Slide 14: Executing an Instruction
But if there is a jump/branch in the code, the increment will be
different
The CPU then acts on the instruction in the IR
1st , the type of instruction is determined by the control unit
The instruction could be one which
  Move data around (e.g. a=b;)
  Combine to operands (e.g. c=a+b;)
  Manipulate one operand (e.g. bit shift/rotation)
  Does a test/comparison and changes the program flow
Other type of instructions are used to
  Call in a new procedure or function (need to change PC)
  Do I/O
  Control loops
  Do other special operation

## Slide 15: .
Once the type of instruction has been deduced, any data needed must be fetched from the memory
  To do a + b, the add instruction needs to fetch data items a and b from the memory
  This is done in the same way as the instruction was fetched
  The operating system has assigned each variable a memory address
Each variable is fetched from the memory and loaded into one of the
local registers within the CPU
  Some instructions on some machines can operate directly on the contents of the memory
Once the variable is loaded, the control unit configures the ALU (or any appropriate functional unit) to execute the operation
The result of the operation is usually stored in one of the registers but
can be written directly to the memory in some architectures
Some operations change the PC differently
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 16: Executing an Instruction
Examples of instruction set
ADD - Add two numbers together.
COMPARE - Compare numbers.
IN - Input information from a device, e.g., keyboard.
JUMP - Jump to designated RAM address.
JUMP IF - Conditional statement that jumps to a designated RAM address.
LOAD - Load information from RAM to the CPU.
OUT - Output information to device, e.g., monitor.
STORE - Store information to RAM.

## Slide 17: .
Once the type of instruction has been deduced, any data needed must be fetched from the memory
  To do a + b, the add instruction needs to fetch data items a and b from the memory
  This is done in the same way as the instruction was fetched
  The operating system has assigned each variable a memory address
Each variable is fetched from the memory and loaded into one of the local registers within the CPU
  Some instructions on some machines can operate directly on the
contents of the memory
Once the variable is loaded, the control unit configures the ALU (or any appropriate functional unit) to execute the operation
The result of the operation is usually stored in one of the registers but can be written directly to the memory in some architectures
Some operations change the PC differently, e.g.
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 18: .
Branches and Jumps
Example
if (a==b)
...run the code starting at address x (PC=x)
else
...run the code starting at address y (PC=y) end
  The result of the conditional determines which branch the
program takes
If we reach the last statement of the loop, we need to jump back to the start
  This also requires that the PC be changed
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 19: .
Next Instruction
Once the result of the operation is known, and any changes to the PC is made, the next instruction can be executed
It follows the same procedure, exactly
Instruction cycle is simple, we can write a simple pseudo- code to describe the cycle more aptly
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 20: .
Pseudo-code for Instruction Cycle
PC = entry_point; //set the starting point While (program_is_running) {
IR = memory(PC); PC = PC + 1;
//load next instruction
//increment PC
itype = type(IR); //find type of instruction
data_loc = find_data(IR,itype);
//get data location, (-1 if none)
if (data_loc >= 0) {//if data is needed data = memory(data_loc) //fetch it
}
execute(itype,data) //execute the instruction
}
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 21: Instruction Set/ Instruction Set Architecture
The instruction set, also called ISA (Instruction Set Architecture), An instruction set is a group of commands for a CPU in machine language.
the possible instructions for a CPU or a subset of instructions to enhance its performance in certain situations. The instruction set provides commands to the processor, to tell it what it needs to do. The instruction set consists of addressing modes, instructions, native data types, registers, memory architecture, interrupt, and exception handling, and external I/O.
All ISAs are generally similar (in principle) and once you are familiar with one, it is easy to learn others
Some are more difficult to learn – Intel ISA is particularly difficult
Our examples will be based on MIPS ISA

## Slide 22: Types of ISA
There are essentially two philosophical approaches to ISA
• Complex Instruction Set Computers (CISC) – E.g. Intel/AMD
• Reduced Instruction Set Computers (RISC) – E.g. SPARC/MIPS/PowerPC

## Slide 23
RISC vs. CISC
RISC machines have much fewer instructions
  Hardware is optimised to execute the most common language constructs
  Does a few things very well
  Heavy use of pipelining and speculative execution method
  No hardware support for high-level constructs
  Harder to write compilers
  Harder to code complex operations
Our study of ISA will be based MIPS
  MIPS is a RISC processor, with
  Fewer instructions to deal with, and
  Simple instruction format that is
  Uniform and easy to understand
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 24: .MIPS Architecture
MIPS processors are used widely in embedded systems (e.g. playstation)
32-bit word length
Contains 32 general-purpose registers, $r0 - $r31
  $r0 is special and always contains the value zero
Most operations can only be on, and store results to, the registers
  There are special instructions for transferring data to/from
memory
There are a total of about 60 instructions, depending on which variant of MIPS you study
Super-pipelined architecture divides each instruction into
small chunks which
  Allows the clock speed to be increased
  Increases throughput of instructions
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 25: .
Types of MIPS Instructions
The instructions of MIPS processors can be divided into 8 broad categories
  Load/Store Instructions
    Fetch/store items from/to memory
    Variants work on whole or part-words
  Arithmetic Instruction
    Addition etc. of two variables
    Comparisons
  Immediate Arithmetic Instructions
    Adding/comparing to constants
  Shift Instructions
    Bit-rotation
  Multiply/divide Instructions
    Multiplications and divisions
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 26: .
Types of MIPS Instructions
Jump and Branch Instructions
  Used to call subroutines,
  Take branches in the code, and
  Execute loops
Coprocessor Instructions
  Send data to (or pass control to) an external coprocessor
Special Instructions
– We will look at how to use a few of the more common instructions and how they relate to the high-level code that you write
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 27: .
An Example: Simple Addition
Consider a simple code fragment
a = b + c;
There is an instruction add which is useful here
As a first pass, we will write this as
add a, b, c
This instruction adds b and c and places the result in a
This is not quite correct: add instruction does not understand the meaning of a, b, c
It needs to know where they are
  Somewhere in the memory
  We use the notation &a to denote the memory address of a
  Then we can write
add &a, &b, &c
This almost correct, but there is another consideration:
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 28: .
Most MIPS instructions can only access the registers, not the main memory
  add is one of such instructions
We need to fetch the data from the main memory first
  If the variable is accessed a lot, the compiler may choose to store it in one of the registers
  But this will not normally be the case
  The instruction we need is:
lw $rx, &a
This belongs to the category of Load/Store instructions
Load the word at location &a (i.e. the variable a) and put it into register $rx (where x ranges from 1 to 31)
There is also the analogous ‘store word’ instruction:
sw $rx, &a
This takes the contents of $rx and transfers them to memory location &a
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 29: .
So our code for a = b + c; will look like:
lw $r1, &b lw $r2, &c
add $r3, $r1, $r2
//load b to r1
//load c to r2
//add the contents of r1 and r2 and place the result in r3
//store the content of r3 to memory location of a
sw $r3, &a
Rmks
The actual values of the addresses &a, &b etc. are determined by the operating system at run-time
What if we have a = b + c – d; ?
We will need another instruction to do the subtraction
sub $rx, $ry, $rz
This subtracts the contents of $rz from the contents of $ry and puts the result in $rx
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 30: .
Addition and Subtraction
a = b + c – d;
We need to break this down into machine instructions
lw | $r1, | &b | //load b to r1
lw | $r2, | &c | //load c to r2
lw | $r3, | &d | //load d to r3
add $r4, $r1, $r2
//add the contents of r1 and r2 and
place the result in r4
//subtract the contents of r3 from the contents r4 and place the result in r5
//store the content of r5 to memory
location of a
sub $r5, $r4, $r3
sw $r5, &a
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng