## Slide 1
CSC2231 COMPUTER ARCHITECTURE
Lecture slides 3

## Slide 2: MIPS Architecture
Last lecture was about what happens inside the processor when a piece of code is executed
  Execution cycle
  Instruction set architecture
  MIPS Architecture
  Types of MIPS Instruction
Today’s lecture more types of MIPS Instruction.
UNIVERSITY, KANO
www.buk.edu.ng
1
www.buk.edu.ng

## Slide 3: www.buk.edu.ng
Immediate Arithmetic instruction
An immediate instruction uses a constant number as one of the
inputs instead of a register operand
To use the Add instruction we have seen so far, we would have to load a constant from memory to use one
example
  So our code for a = b + c; will look like:
addi $r1, $r2,20
//add the contents of r2 and 20 and place the result in r1
// $r1= $r2 + 20
Rmks
- By including constants inside arithmetic instructions, operations are much faster and use less energy than if constants were loaded from memory
UNIVERSITY, KANO
2
www.buk.edu.ng

## Slide 4: Multiplication and Division
Multiplication and Division
Add and Sub are performed on 32 bit numbers held in the general purpose registers (32bit each)
The result is a 32bit number itself
Multiplication and Division may generate results that are larger than 32bits
The MIPS architecture provides 2 special 32bit registers that are the destination for the multiplication and division instructions. These registers are called
  hi and lo
    hi holds the higher 32bits of the results
    lo holds the lower 32bits of the results
UNIVERSITY, KANO
www.buk.edu.ng
3
www.buk.edu.ng

## Slide 5: Multiplication and Division
Special instructions are also provided to move data from these
registers into the special purpose ones ($r0 t0 $r31)
  mfhi register & mflo register to move from hi, lo to another register
Multiplication Example Program
  in c : a = b * c
  In MIPS: let b be $r2, let c be $r3 and a be $r1 and $s1(since it
maybe upto 64 bits)
mult $r2, $r3 mfhi $r1 mflo $r2
/ / b *c
/ / upper half of product into $r1
/ / lower half of product into $r2
UNIVERSITY, KANO
www.buk.edu.ng
4
www.buk.edu.ng

## Slide 6
.
Syntax of division
div register1, register2
divides 32bit register1 by 32bit register2
Puts remainder of division in hi, quotient in lo Division Example Program
div $r2, $r3
mfhi $r1 mflo $r2
/ / lo = $r2/$r3 hi = $r2 mod $r3
/ / $r1= hi
/ / $r2 = lo
UNIVERSITY, KANO
www.buk.edu.ng
5
www.buk.edu.ng

## Slide 7
.
Shift instructions
move all the bits in a word to the left or right, filling the emptied bits with 0s
They belong to a class of operations called logical operations
The actual name of the MIPS shift instructions are called
  Shift left logical sll
  Shift right logical srl
–
www.buk.edu.ng
UNIVERSITY, KANO
www.buk.edu.ng
Bayero University, Kano - Nigeria

## Slide 8
.
Example
If register $r1 contained
0000 0000 0000 0000 0000 0000 0000 1001 = 9
and the instruction to shift left by 4 was executed the new value would be
0000 0000 0000 0000 0000 0000 1001 0000 = 144
Code
Sll s$r2 , $r1, 4 //reg $r2 = reg $r1 << 4 bits
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 9: .
Other MIPS logical instructions
And
performs a logical bit-by-bit operation with 2 operands that calculates a 1 only if there is a 1 in both operands
and $r1, $r2, $r3 // reg $r1 = reg $r2 & reg $r3
Or
A logical bit-by-bit operation with 2 operands that calculates a 1 if there is a 1 in either operand
or $r1, $r2, $r3 // reg $r1 = reg $r2 | reg $r3
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 10: .
Constants are useful in AND and OR logical operations as well as arithmetic operations, so MIPS also provides the instructions
and immediate andi
or immediate ori
Other instructions include Not, Nor and Xor
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 11: Branch and jump instructions
Branch Instructions
Branch instructions allow programmers to design decision making ability into a program
For that reason they can be referred to as program control instructions since they support the ability for a program to determine when to change operation.
In general, a branch performs a comparison. If the comparison is successful, the next instruction executed is at another point in the program
If the desired comparison is not achieved the program simply executes the instruction following the branch
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 12: www.buk.edu.ng
The following list is not complete, but composes a relatively useful group of the branch instruction subset.
beq – branch on equal
beq $r1, $r2, label //if the content of r1= r2, branch to label; otherwise
execute next instruction
bgez- branch on greater than or equal zero
bgez $r1, label //if the content of r1 is >= 0 branch to label; otherwise execute next instruction
bgtz - branch on greater than zero
bgtz $r1, label //if the content of r1> 0, branch
nextinstruction
Other instructions include :
; otherwise execute
blez - branch on less than or equal to zero bltz - branch on less than zero
UNIVERSITY, KANO
www.buk.edu.ng

## Slide 13: .
bne- branch on not equal
beqz- branch on equal zero
bge- branch on greater than or equal
bgt- branch on greater than
ble- branch on less than or equal
blt- branch on less than
bnez- branch on not equal zero
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 14: .
An Example : simple branch
consider an if statement fragment
if (i == j) f = g + h; else f = g – h;
The first expression compares for equality, so it would seem that we would want beq. In general, the code will be more efficient if we test for the opposite condition to branch over the code that performs the subsequent then part of the if
bne $r1,$r2,Else
// go to Else if i is not equal to j
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 15: .
The next assignment statement performs a single operation, and if all the operands are allocated to registers, it needs just one instruction:
add $r3,$r4,$r45 // f = g + h (skipped if i is not equal to j)
We now need to go to the end of the if statement
j Exit // go to Exit
This example introduces another kind of branch, often called an unconditional branch. This instruction says that the processor always follows the branch. To distinguish between conditional and unconditional branches, the MIPS name for this type of instruction is jump, abbreviated as j
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 16: www.buk.edu.ng
Jump instructions
This transfer is unconditional
  There is no option on jump instructions; a jump is always to a
labeled location
  J loop // the next instruction executed is the one labelled loop
There are different variations of jump instruction, some maybe used for subroutine or procedure calls
There are different variations of jump instruction, some maybe used for subroutine or procedure calls
procedure is a stored subroutine that performs a specific task based on the parameters with which it is provided
UNIVERSITY, KANO
www.buk.edu.ng

## Slide 17: www.buk.edu.ng
MIPS assembly language includes an instruction just for the procedures
it jumps to an address and simultaneously saves the address of the following instruction in a special register $ra, The jump-and-link instruction jal
Example
jal loop // jump to loop and save the content of PC in $ra
The link portion of the name means that an address or link is formed that points to the calling site to allow the procedure to return to the proper address.
This “link,”stored in register $ra, is called the return address. The return address is needed because the same procedure could be called from several parts of the program
www.buk.edu.ng
16
UNIVERSITY, KANO
Bayero University, Kano - Nigeria

## Slide 18: .
MIPS use a jump register instruction (jr), meaning an unconditional jump to the address specified in a register:
jr $ra // jump to the address specified in $ra
Consider a simple for loop
for (i>0; i<=x; i++){ y = y + i;
}
// More stuff
After doing y = y + i; need to unconditionally jump back to the start of the loop
- j &jal,jr does exactly that
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 19: .
Set Instructions
The set instructions are used in decision-making functions( often with branch instructions) within a program
These instructions instruction that compares two registers and sets a third register to 1 if the first is less than the second; otherwise, it is set to 0
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 20: .
– Example
A common use of if…else clauses is to set flags:
if(x < y) {
flag = 1;
}
else {
flag = 0;
}
Easy to do using:
slt $r1, $r2, $r3 : “set-on-less-than”
Sets r1=1 if r2<r3, else sets r1=0
// Load x into r1
// Load y into r2
// r3=1 if r1<r2, else r3=0
www.buk.edu.ng// Store r3 as flag
lw $r1, &x lw $r2, &y
slt $r3, $r1, $r2
Bayero sUnwivers$ityr, Ka3no,- Ni&gefrialag
19
UNIVERSITY, KANO
www.buk.edu.ng

## Slide 21: .
MIPS instruction coding
MIPS instructions are classified into four groups according to their coding formats
R-type : this group contains all instructions that do not require an immediate value, target offset, memory address displacement or memory address to specify an operand. This includes arithmetic and logic with all operands in registers, shift instructions and register direct jump instructions (jalr, jr)
I-type this group includes instructions with an immediate operand, branch instructions, load and store. In MIPS architecture all memory accesses are handled by the main processor , so coprocessor load and store instructions are included in this group
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng

## Slide 22: .
J-type this group consist of the two direct jump instructions ( j and jal). These instructions require a memory address to specify their operand
Coprocessor instructions MIPS processors all have two standard coprocessors CP0 and CP1. CP0 processes various kinds of program exceptions while CP1 is a floating point processor
UNIVERSITY, KANO
www.buk.edu.ng
www.buk.edu.ng